## Slide 1: Minesweeper Lab
Slides and Assignment
By: Austin Crapo
Date: June 2017

## Slide 2
What is it?
The original and most basic version of the game was called ‘Cube’ and was published in the 1960’s
The concept was refined and caught on as a successful puzzle game in the 1970’s
A player must reveal all empty tiles on a grid.
A revealed empty tile states how many of its 8 neighbors contain a bomb.
Revealing an empty tile where all neighbors are also empty reveals all its neighbors.
If a player reveals a bomb, they lose.
A running timer gives time pressure.
If the timer runs out before the last empty tile is revealed, all the bombs ‘go off’ and the player loses.
Picture taken from http://www.wikihow.com/Cheat-at-Minesweeper July 19 2017 and used under fair use

## Slide 3: GLIM
Graphics are provided via the terminal
GLIM is a library that uses terminal ‘escape sequences’ to print characters to arbitrary positions with one of 256 colors.
Almost all the code to handle graphics is provided in the file common.s.
The solution only used the library to print a win or lose statement at the end of the game.
Graphics Library for MIPS

## Slide 4: MIPS Interrupts
What are interrupts?
Asynchronous code segments that:
Run when a specific signal occurs
Run immediately
Keyboard Interrupts:
Run when a key is pressed
Timer Interrupts:
Run when a timer goes off
Timer gif from: http://amightynut.blogspot.ca/2013/12/animated-gif-digital-timer.html

## Slide 5: Coprocessor 0
Coprocessor 0
$9
$11
$13
$12
$14
Timer Counter
Timer Compare
Status Register
Cause Register
EPC
TODO: add basic operation of timer.
This counter is incremented
every 10ms
When the counter is
equal the compare value
an exception is generated
Notes: This and the remaining slides are graphical explanations of using the coprocessor for interrupts. Provided by J. Nelson Amaral. For questions on slide meanings and to see the portions that deal with the display interrupts, please speak with him.

## Slide 6
0xffff 0000
Control Register
0xffff 0004
Data Register
Keyboard
Exception
Handler
main
Coprocessor 0
$9
$11
$13
$12
$14
Initialize
Status Register
Enable Keyboard
Interruptions
Initialize
Clock

## Slide 7
0xffff 0000
Control Register
0xffff 0004
Data Register
Keyboard
000
001
010
011
100
101
110
111
000
001
010
011
100
101
110
Coprocessor 0
$9
$11
Exception
Handler
main
$13
$12
$14
Read
Keyboard
Data
Keyboard
Interrupt

## Slide 8
0xffff 0000
Control Register
0xffff 0004
Data Register
Keyboard
000
001
010
011
100
101
110
111
000
001
010
011
100
101
110
Coprocessor 0
$9
$11
Exception
Handler
main
$13
$12
$14
Is it “q”, something else?
Do the right thing.
Re-enable
Keyboard
Interrupts
Reset
Status
and
Cause
Register

## Slide 9
0xffff 0000
Control Register
0xffff 0004
Data Register
Keyboard
000
001
010
011
100
101
110
111
000
001
010
011
100
101
110
Coprocessor 0
$9
$11
Exception
Handler
main
$13
$12
$14
Timer
Interrupt
Reset
Timer
Reset
Status
and
Cause
Register

## Slide 10: The Assignment – common.s
Number of rows for this session: 20
Number of columns for this session: 40
Random seed to use: 5
Number of bombs for this session: 100

## Slide 11: List of Characters

## Slide 12
row
col
getTile
Address of
character that
represents the tile
State of
the tile
?

## Slide 13
row
col
hasBomb
1: has bomb
0: has no bomb

## Slide 14
row
col
setBomb

## Slide 15
prepareBoard
Invoked once after setting bombs.
May or may not be needed.

## Slide 16
row
col
printTile

## Slide 17
main
(and exception handler)
See specification in lab instructions.